## Slide 1
Topics will Be Covered:
Open and Short Circuit
Series Parallel DC Circuit
REDUCE AND RETURN APPROACH
BLOCK DIAGRAM APPROACH
Ladder Networks

## Slide 2
6.8 OPEN CIRCUITS
An open circuit is two isolated terminals not connected by any kind of element.
An open circuit can have a potential difference (voltage) across its terminals, but the current is always zero (0) amperes.
EXAMPLE 6.27.1 Determine the unknown voltage (V) and current (I) for the following network.
Ioc = 0 A Roc =  (Infinite)

## Slide 3
3
6.8 Short CIRCUITS
A short circuit is a very low resistance, direct connection between two terminals of a network.
Aa short circuit can carry a current of a level determined by the external circuit, but the potential difference (voltage) across its terminals is always zero (0) volts.
EXAMPLE 6.27.2 Determine the unknown voltage (V) and current (I) for the following network.
Vsc = 0 A Rsc = 0 (Zero)

## Slide 4
4
EXAMPLE 6.28.1 Determine the unknown voltage (V) and current (I) for the following network.
Due to the open circuit, the current flow (I3) through the R3 is zero. Thus, the current I flows through R1 and R2 and V is equal to the voltage drop across the resistance R2.
EXAMPLE 6.28.2 Determine the unknown voltage (V) and current (I) for the following network.
Due to the open circuit, the current flow (I3) through the R3 is zero and since R2 is shorted the current flow (I2) through the R2 is zero. Thus, the current I flows through R1 and short circuit and V = 0 V.
I3=0
I
V3=0
I3=0
I2=0
I
I
V3=0
I

## Slide 5
Problem 38 [Ch 6] A For the network in Fig. 6.108:
(a) Determine Is and VL.
(b) Determine Is if RL is shorted out.
(c) Determine VL if RL is replaced by an open circuit.
(b)
(c)

## Slide 6
6
Problem 39 [Ch 6] For the network in Fig. 6.109:
a. Determine the open-circuit voltage VL.
b. If the 2.2 k resistor is short circuited, what is the new value of VL?
c. Determine VL if the 4.7 k  resistor is replaced by an open circuit.

## Slide 7
7
7.3 REDUCE AND RETURN APPROACH

## Slide 8
8
EXAMPLE 7.1 Find current I3 for the series-parallel network in Fig. 7.3.
Solution: Checking for series and parallel elements, we find that resistors R2 and R3 are in parallel. Their total resistance is:
Redraw the circuit showing the calculated resistance R4.
Now, resistors R1 and R4 are in series, resulting in a total resistance of
The source current is then determined using Ohm’s law:
Returning to Fig. 7.3, we find the current I3 as follows:

## Slide 9
9
Solution:
Practice Book Problem [SECTIONS 7.2–7.5 Series Parallel Networks] Problems: 1 ~ 24

## Slide 10
10
7.4 BLOCK DIAGRAM APPROACH

## Slide 11
11
EXAMPLE 7.4 Determine all the currents and voltages for the series-parallel network in Fig. 7.12.
Solution:

## Slide 12
12
EXAMPLE 7.7
a. Find the voltages V1, V3, and Vab for the network in Fig. 7.20. b. Calculate the source current Is.
Solution:

## Slide 13
13
EXAMPLE 7.8 For the network in Fig. 7.22, determine the voltages V1 and V2 and the current I.
Solution:
Applying Kirchhoff’s voltage law:
Applying Kirchhoff’s voltage law:

## Slide 14
14
Problem 10:
a. Find the magnitude and direction for current I, I1, I2, and I3, for the network in Fig. 7.70.
b. Indicate their direction on Fig. 7.70.
Solution: Voltage drop across the resistance R1 equal to 24 V. So:
Voltage drop across the resistance R3 equal to 8 V. So:
According to KCL: I = I1 + I2 = 6 A + 16 A = 22 A
Practice Book Problem [SECTIONS 7.2–7.5 Series Parallel Networks] Problems: 1 ~ 24
Voltage drop across the resistance R2 equal to the difference of 24 V and 8 V. So:

## Slide 15
15
7.6 LADDER NETWORKS

## Slide 16
16
A n-section ladder network appears in the following Figure.
The reason for the terminology is quite obvious for the repetitive structure.
Basically, two approaches are used to solve networks of this type.
(1) Calculate the total resistance and resulting source current, and then work back through the ladder until the desired current or voltage is obtained [Reduce and Return Approach].
(2) Assign a letter symbol to the last branch current (In) and voltage (Vn) and work back through the network to the source, maintaining this assigned current or other current of interest. The desired current can then be found directly.

## Slide 17
17
EXAMPLE FIG. 7.3 Determine the unknown currents Is, I2, I3, I4, and I6 and voltage (V6) for the following network.
(a)
(b)
(c)
Method 1

## Slide 18
18
(d)
From Fig. (c), we have:
From Fig. (a), we have:

## Slide 19
19
Method 2
The assigned notation for the current through the final branch is I6:
Practice Problem [SECTIONS 7.6] Problems: 25 ~ 28

## Slide 20
20
8.3 SOURCE Transformation

## Slide 21
21
Voltage Source Convert to Current Source
Current Source Convert to Voltage Source

## Slide 22
22
Practice Book [Ch 8]
Problem: 7 ~ 10 and 14

## Slide 23
23
EXAMPLE 8.3.1 Using the source conversion find the value of voltage V6.

## Slide 24
24
More Examples Related to
Series-Parallel Circuits

## Slide 25
25
Problem 12 [Ch 7]: For the network in Fig. 7.72: a. Determine the current I1. b. Calculate the currents I2 and I3. c. Determine the voltage levels Va and Vb.

## Slide 26
26
Problem 10 [Ch 7] Determine the unknown voltage (V) and current (I) for the following network.
Vsc=0

## Slide 27
27
Problem 26 For the ladder network in Fig. 7.86: a. Determine RT. b. Calculate I. c. Find I8. d. Power consumed by R6 resistance. e. Power delivered by the 2 V supply.

## Slide 28
28