## Slide 1
Network Theorems
Chapter 9 [DC]

## Slide 2
2
9.2 SUPERPOSITION THEOREM

## Slide 3
3
The current through, or voltage across, an element in a linear bilateral network is equal to the algebraic sum of the currents or voltages produced independently by each source.
Steps to Apply Superposition Theorem
Step 1: | Select a single source acting alone. Short the other voltage sources to make voltage is zero and open the current sources to make current is zero, if internal resistance/impedances are not known. If known, replace them by their internal impedances.
Step 2: | Find the current through or the voltage across the required element, due to the source under consideration, using a suitable simplification technique.
Step 3: | Repeat the above two steps for all the sources.
Step 4: | Add all the individual effects produced by individual sources, to obtained the total current in or voltage across the element.
Statement of Superposition Theorem
I = 0
E = 0

## Slide 4
4
Solution: Consider E then and I = 0 A (open).
Consider I then and E = 0 V (shorted).
According to Superposition Theorem:

## Slide 5
5

## Slide 6
6

## Slide 7
7
Solution: Consider E1 then E2 = 0 V (shorted) and I3 = 0 A (open).
I3 = 0
E2 = 0
V31
Example 9.2.1 Using superposition, find the voltage V3 for the following network.
Consider E2 then E1 = 0 V (shorted) and I3 = 0 A (open).

## Slide 8
8
E2 = 0
E1 = 0
V33
According to Superposition Theorem:
Consider I3 then E1 = 0 V (shorted) and E2 = 0 V (shorted).
Practice Book [Ch 9] Problem: 1 ~ 6

## Slide 9
9
9.3 THÉVENIN’S THEOREM

## Slide 10
10
Any two-terminal, linear bilateral network can be replaced by an equivalent circuit consisting of a voltage source and a series resistance/impedance, as shown in the following figure.
Statement of Thevenin’s Theorem
RTh: Thevenin’s equivalent resistance
ETh: Thevenin’s equivalent voltage
ZTh: Thevenin’s equivalent impedance
ETh: Thevenin’s equivalent voltage

## Slide 11
11
Steps to Apply Thevenin’s Theorem
Step 1: | Remove that portion of the network where the Thévenin equivalent circuit is found.
Step 2: | Mark the terminals of the remaining two-terminal network. (The importance of this step will become obvious as we progress through some complex networks.)
Step 3: | Calculate RTh/ZTh by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance/impedance between the two marked terminals. (If the internal resistance/impedance of the voltage and/or current sources is included in the original network, it must remain when the sources are set to zero.)
Step 4: | Calculate ETh by first returning all sources to their original position and finding the open-circuit voltage between the marked terminals. (This step is invariably the one that causes most confusion and errors. In all cases, keep in mind that it is the open circuit potential between the two terminals marked in step 2.)
Step 5: | Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.
Step 6: | Do the remaining required calculation

## Slide 12
12
Example 9.6 Find the Thévenin equivalent circuit for the network in the shaded area of the network in Fig. 9.26. Then find the current through RL for values of 2 , 10 , and 100 .
Step 1: Remove that portion of the network where the Thévenin equivalent circuit is found.
Step 2: Mark the terminals (such as a and b) of the remaining two-terminal network.
Step 3: Calculate RTh by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance between the two marked terminals (a and b).

## Slide 13
13
Step 4: Calculate ETh by first returning all sources to their original position and finding the open-circuit voltage between the marked terminals (a and b).
Step 5: Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.

## Slide 14
14
Step 1: Remove that portion of the network where the Thévenin equivalent circuit is found.
Step 2: Mark the terminals (such as a and b) of the remaining two-terminal network.
Step 3: Calculate RTh by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance between the two marked terminals (a and b).
Example 9.8 Using Thevenin’s Theorem calculate the current passing through the resistor R4.

## Slide 15
15
Step 4: Calculate ETh by first returning all sources to their original position and finding the open-circuit voltage between the marked terminals (a and b).
Step 5: Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.
Step 6: Calculate the current passing through the resistor R4.

## Slide 16
16
Example 9.3.1: Find the Thévenin equivalent circuit for the portions of the following network to points a and b.
Step 1 and Step 2:
Step 3: RTh calculation
Step 4: ETH calculation

## Slide 17
17
Step 5: Draw the Thévenin equivalent circuit
Practice Book [Ch 9] Problem: 7 ~ 15