## Slide 1
Topics will Be Covered:
Waveforms
Generation of Sine Waveform
Definitions Related to Waveforms
General Format of Mathematical Equation for the Sinusoidal Voltage/Current with Zero Degree Initial Angle
General Format of Mathematical Equation for the Sinusoidal Voltage/Current with Phase Angle
Phase Difference and Phase Relation Between Two Waveforms

## Slide 2
Chapter 13
Sinusoidal Alternating Waveforms

## Slide 3
3
Waveforms
Waveform: The path traced by a quantity, such as the voltage, current etc. as a function of some variable such as time (as above), position, degrees, radians, temperature, and so on.
(1) Waveform Based on the Following Sine Rule
Sinusoidal
Non-sinusoidal
Unidirectional
Bidirectional
(2) Waveform Based on Direction of Propagation
Periodic
Aperiodic
(3) Waveform Based on Periodicity
(4) Waveform Based on the Shape
Symmetrical
Asymmetrical

## Slide 4
4
Faradays Law of Electromagnetic Induction:
Faradays First Law: Whenever a conductor is placed in a varying magnetic field an electromotive force (EMF) is induced or produced or developed across the conductor (called as induced emf), and if the conductor is a closed circuit, then induced current flows through it.
Faradays Second Law: The magnitude of induced emf is equal to the rate of change of flux linkages (d/dt) with the coil. So, induced emf: e = N(d/dt) V.
where, Em=Blv is constant.
e(t) = Blvsin V = Emsin V
So, e(t)  sin V
(b) Generated waveform by a generator
(a) Simple construction of a generator
Magnitude of Induced voltage affected by flux density (B), the effective length of conductor (l), the conductor velocity (v) and sine of angle between flux line and the direction of motion of conductor.
The average value of AC quantity is zero.
Generation of Sine Waveform

## Slide 5
5
Instantaneous Value: The magnitude of a waveform at any instant of time is called instantaneous value.
Instantaneous value is denoted by lowercase letters [such as e for sources of voltage, v for the voltage drop across a load, i for the current pass through a load and p for the power]. In Fig. 13.3, e1 = 64.7 V and e2 = 56.5 V are instantaneous value of e at time t1 = 0.06 s and t2 = 0.25 s.
Peak or Crest or Amplitude or Maximum Value: The maximum instantaneous value attained by an alternating quantity during positive and negative half-cycle is called its amplitude or peak or crest or maximum value.
Peak value is denoted by uppercase letters [such as Em, Vm and Im]. In Fig. 13.3, Em = 80 V peak value of e.
Fig. 13.3 Important parameters for a sinusoidal voltage.
Peak-to-Peak Value: The full voltage between positive and negative peaks of the waveform, that is, the difference between the positive peak and the negative peak.
Peak-to-Peak value is denoted by uppercase letters [such as Ep-p, Vp-p and Ip-p]. In Fig. 13.3, Ep-p = 80 V  ( 80 V) = 160 V peak-to-peak value of e.
Some Definition Related to Waveforms

## Slide 6
6
Fig. 13.3 Important parameters for a sinusoidal voltage.
Periodic Waveform: A waveform that continually repeats itself after the same time interval. The waveform in Fig. 13.3 is a periodic waveform.
Cycle: The portion of a waveform that continually repeats itself after the same time interval is called a cycle.
The cycles within T1, T2, and T3 in Fig. 13.3 may appear different in Fig. 13.4, but they are all bounded by one period of time and therefore satisfy the definition of a cycle.
Period (T): The time taken by an alternating quantity to complete its one cycle is known as time period.
It is denoted by T seconds. After every seconds, the cycle of an alternating quantity repeats.

## Slide 7
7
Frequency (f): The number of cycles completed by an alternating quantity per second is known as frequency.
It is denoted by f and it is measured in cycle/second which is known as Hertz, denoted by Hz.
Relation between Frequency and Time Period: Frequency is reciprocal of time period.
t = s = s
Angular Frequency or Velocity (): The rate of change of angular position is called angular frequency or angular velocity. Unit of angular frequency is rad/s.
Relation Between Degree and Radian:
In the world, some countries (Bangladesh, India, Argentina, Australia, Combodia etc.) use 50 Hz and some countries (USA, Canada, Brazil, Haiti, Eucador, Colombia, Costa Rica etc.) use 60 Hz as power frequency.
The frequency of DC voltage is zero (0) Hz.

## Slide 8
8
Relation among Angular Frequency, Frequency and Time Period:
Alternating Current/Voltage:
Alternating current/voltage rises from zero to a maximum value in one direction and decreases back to zero. It then rises to the same maximum value in the opposite direction and again decreases to zero. These values are repeated again and again at equal intervals of time.
The average value of AC quantity is zero.
It is seen from the following figure that the abscissa (x-axis) of alternating voltage and current can be represent in terms of time (t), angle () in deg., or angle () in rad.

## Slide 9
9
EXAMPLE 13.5 Determine the frequency and period of the sine wave having an angular frequency of 500 rad/s.
Solution: We know that,  = t, thus s
However  must be converted to rad., since is  rad/s.
= s = 1.57 rad
Solution: We know that,  = t or
Practice Problem 4 ~ 16 [P582]

## Slide 10
10
General Format of Mathematical Equation for the Sinusoidal Voltage or Current with Zero Degree Initial Angle

## Slide 11
11
Induced EMF:
e(t) = Emsin V = Emsint V
= Emsin2ft V = Emsint V
Example: e(t) = 20sin31.4t mV
Voltage Drop:
v(t) = Vmsin V = Vmsint V
= Vmsin2ft V = Vmsint V
Current:
i(t) = Imsin A = Imsint A
= Imsin2ft A = Imsint A
Example: v(t) = 60sin100t V
Example: i(t) = 10sin261.67t A
General Format of Mathematical Equation for the Sinusoidal Voltage or Current
Em = 20 mV;  = 31.4 rad/s
Vm = 60 V;  = 100 rad/s
Im = 10 A;  = 261.67 rad/s
f = (31.4 rad/s)/2 = 5 Hz
f = (100 rad/s)/2 = 50 Hz
f = (261.67 rad/s)/2 = 41.67 Hz
T = 1/(5 Hz) = 0.2 s
T = 1/(50 Hz) = 0.02 s or 20 ms
T = 1/(41.67 Hz) = 24 ms
0 6 12 18 24 30 t [ms]
10
10
it) [A]
0 5 10 15 20 25 t [ms]
60
60
v(t) [V]
0 0.05 0.1 0.15 0.2 0.25 t [s]
20
20
e(t) [mV]
0 90o 180o 270o 360o 450o  [deg.]
20
20
e(t) [mV]
/2  3/2 2 5/2  [rad.]
0 90o 180o 270o 360o 450o  [deg.]
60
60
v(t) [V]
/2  3/2 2 5/2  [rad.]
0 90o 180o 270o 360o 450o  [deg.]
10
10
i(t) [A]
/2  3/2 2 5/2  [rad.]

## Slide 12
12
EXAMPLE 13.8 Given, e(t) = 5sin V, determine e(t) at (a)  = 40o, (b)  = 0.8, and (c) t = 13 ms if the angular frequency is 314 rad/s.
Solution: For  = 40o,
e(t) = 5sin(40o) = 5 (0.6428) = 3.21 V
For  = 0.8 = (180o/)(0.8) = 144o
e(t) = 5sin(144o) = 5(0.6428) = 3.21 V
For t = 13 ms and 314 rad/s,
 = t = (314)(1310-3) rad.
= (314)(1310-3)(180o/) deg. = 234o
e(t) = 5sin(234o) = 4.05 V
Solution: (a) According to question we can write,
v(t) = 10sin = 4 V
However, Fig.13.19 reveals that the magnitude of 4 V (positive) will be attained at two points between 0° and 180°. The second intersection is determined by

## Slide 13
13
Solution:
(a) Peak Value: Vm = 8 V
(b) Instantaneous value at 0.3 s is 8V
Instantaneous value at 0.6 s is 0 V
(c) Peak-to-peak Value: Vp-p =2Vm = 16 V
(d) Period: T = 0.4 s
(e) Number of cycle: (1.4s/0.4s) = 3.5 cycles
(f) Frequency: f =1/T = 1/(0.4 s) = 2.5 Hz
(g) Angular Frequency:  = 2f = 15.7 rad/s
(h) Instantaneous Equation:
v(t) = 8Vsin V = 8Vsin15.7t V

## Slide 14
14
50 Hz
g. 314 rad/s
h. i(t) = 20mAsin = 20mAsin314t

## Slide 15
15
PROBLEM 18 [P582] Sketch i(t) = 5sin754t A with the abscissa: a. angle in degrees, b. angle in radians, and c. time in seconds.
Solution: Here, Im = 5 A,  = 754 rad/s.
T = 2/ = 2/754 = 8.33 ms
0 90o 180o 270o 360o 450o  [deg.]
5
5
i(t) [A]
0 /2  3/2 2 5/2  [rad.]
5
5
i(t) [A]
0 2.08 4.17 6.25 8.33 10.41 t [ms]
5
5
i(t) [A]
PROBLEM 19 [P582] Sketch i(t) = 7.6sin43.6t A with the abscissa: a. angle in degrees, b. angle in radians, and c. time in seconds.
Solution: Here, Im = 7.6 A,  = 43.6 rad/s.
T = 2/ = 2/43.6 = 144 ms
Practice Problem 17 ~ 24 [P582]
0 90o 180o 270o 360o 450o  [deg.]
i(t) [A]
7.6
7.6
i(t) [A]
7.6
7.6
0 /2  3/2 2 5/2  [rad.]
i(t) [A]
7.6
7.6
0 36 72 108 144 180 t [ms]

## Slide 16
16
General Format of Mathematical Equation for the Sinusoidal
Voltage/Current with Phase Angle

## Slide 17
17
Mathematical Equation for the Sinusoidal when start Before or After 0°
If the waveform passes through the horizontal axis (y-axis) with a positive-going (increasing with time) slope before 0°, as shown in the following Figures, the expression is
v(t)=Vmsin(+v) V = Vmsin(t+v) V
Vmsinv
v
Vm
(v)
(2v)
v(t)
e(t)=Emsin(+e) V = Emsin(t+e) V
Emsine
e
Em
(e)
(2e)
e(t)
i(t)=Imsin(+i) V = Imsin(t+i) A
Imsini
i
Im
(i)
(2i)
i(t)
If the waveform passes through the horizontal axis (y-axis) with a positive-going (increasing with time) slope after 0°, as shown in the following Figures, the expression is
v(t)=Vmsin(v) V = Vmsin(tv) V
e(t)=Emsin(e) V = Emsin(te) V
i(t)=Imsin(i) V = Imsin(ti) A
Vmsinv
v
v(t)
Vm
(+v)
(2+v)
Emsine
e
e(t)
Em
(+e)
(2+e)
Imsini
i
i(t)
Im
(+i)
(2+i)

## Slide 18
18
Phase Angle and Initial Angle
e(t) = Emsin( + e) V = Emsin(t + e) V
v(t) = Vmsin( + v) V = Vmsin(t + v) V
i(t) = Imsin( + i) A = Imsin(t + i) A
In generally, the instantaneous or time domain equation can be written as follows:
e, v and i are called phase angle.
Initial Angle: The angle from which a waveform started with a positive-going (increasing with time) slope is called initial angle.
Initial Angle =  Phase Angle
e0 =  e; v0 =  v; i0 =  i;
where, e0, v0 and i0 are initial angle.
Remember: To identify the phase angle from an equation, at first +cos,  cos and  sin convert to +sin.
If the waveform is given as cos, cos, and sin must be convert to positive sine wave that means sin using the following relations:
cos = sin( + 90o)
 cos = sin(  90o)
 sin = sin(  180o)
sin( + 90o)
sin(  90o)
sin( + 180o)
sin(  180o)

## Slide 19
19
EXAMPLE Identify the phase angle and find the initial angle for the following waveforms:
(a) e(t) = 20sint V
(b) v(t) = 100cost V
(c) i(t) =  2cost A
(d) v(t) =  150sint V
Phase angle, e = 0o
Initial angle, e0 =  e = 0o
v(t) = 100sin(t + 90o) V
Phase angle, v = 90o
Initial angle, v0 =  v =  90o
i(t) = 2sin(t  90o) A
Phase angle, i =  90o
Initial angle, i0 =  i = 90o
v(t) = 100sin(t  180o) V
Phase angle, v =  180o
Initial angle, v0 =  v = 180o
(e) v(t) = 60cos(t  20o) V
(f) e(t) =  160cos(t  20o) V
v(t) = 60sin(t  20o + 90o) V = 60sin(t + 70o) V
e(t) = 160sin(t  20o  90o) V = 160sin(t  110o) V
Phase angle, v = 70o
Initial angle, v0 =  v =  70o
Phase angle, e =  110o
Initial angle, e0 =  e = 110o
(g) i(t) = 8sin(t + 80o) A
i(t) = 8sin(t + 80o  180o) A
= 8sin(t + 260o) A
= 8sin(t  100o) A
Phase angle or, i = 260o or  100o
Initial angle, i0 =  i =  260o or 100o

## Slide 20
20
EXAMPLE Sketch v(t) = 50sin(261.67t + 60o) V with the abscissa:
a. angle in degrees, b. angle in radians, and c. time in seconds.
Solution: Here, Vm = 50 V,  = 261.67 rad/s, v0 =  v =  60o
24 ms
6 ms
 4 ms
v(t) [V]
50
50
60o 150o 240o 330o 420o 510o  [deg.]
v(t) [V]
50
50
1.05 2.62 4.19 5.76 7.33 8.9  [rad.]
v0 (rad.) == 1.05 rad
50
50
4 2 8 14 20 26 t[ms]
v(t) [V]

## Slide 21
21
EXAMPLE Sketch e(t) = 80sin(157t  30o) V with the abscissa:
a. angle in degrees, b. angle in radians, and c. time in seconds.
Solution: Here, Em = 80 V,  = 157 rad/s, e0 =  e = 30o
40 ms
10 ms
3.33 ms
e(t) [V]
80
80
30o 120o 210o 300o 390o  [deg.]
e(t) [V]
80
80
0.52 2.09 3.66 5.23 6.8  [rad.]
e0 (rad.) == 0.52 rad
e(t) [V]
80
80
3.33 10.33 20.33 30.33 40.33 t[ms]
Practice Problem 25 ~ 26 [P582]

## Slide 22
22
PROBLEM 27 and 28 [P583] Write the analytical expression for the waveforms in Fig. 13.84 with the phase angle in degrees.
 = 260  377 rad/s
e =  e0 = ( 30o) = 30o
Vm = 25 V
Im = 3 mA
 = 21000  6280 rad/s
i =  i0 = ( ) =
i = =
 = 240  251.2 rad/s
e =  e0 = (100o) =  100o
Vm = 0.01 V
Im = 2 mA
 = 210000  62800 rad/s
i =  i0 = ( ) =
i = =
v(t) = 25sin(377t + 30o) V
v(t) = 0.01sin(251.2t  100o) V
i(t) =  3sin(6280t + 120o) mA
i(t) = 2sin(62800t + 135o) mA

## Slide 23
23
Phase Difference and Phase Relation Between Two Waveforms

## Slide 24
24
Conditions to find the Phase difference, Time difference and phase relation between two waveforms:
They must be same type waveforms
Their frequency or angular frequency or time period must be same
Phase Difference and Phase Relation Between Two Waveforms
Angle Difference = Voltage angle  Current Angle
Phase Difference =  Angle Difference 
Case I:
Angle Difference= Voltage angle  Current Angle = 0o
Phase Relation: v(t) and i(t) are in phse.
The starting points of v(t) and i(t) are same.
Case II:
Angle Difference= Voltage angle  Current Angle > 0o
Phase Relation: v(t) leads i(t), or i(t) lags v(t)
v(t) starts before i(t), or i(t) starts after v(t)
Case III:
Angle Difference= Voltage angle  Current Angle < 0o
Phase Relation: v(t) lags i(t), or i(t) leads v(t)
v(t) starts after i(t), or i(t) starts before v(t)

## Slide 25
25
Solution: (i) Angle Difference = (+30°)  (+70°) =  40°
Phase Difference =  40° = 40°
(ii) Angle Difference < 0°; So,
v(t) lags i(t) by 40o, or i(t) leads v(t) by 40o
EXAMPLE 13.12 (a) What is (i) the phase difference, and (ii) the phase relationship between the sinusoidal waveforms of the following sets? (a) v(t) = 10sin(t + 30°) V; i(t) = 5sin(t + 70°) A
(i) Angle Difference = (20°)  (+60°) =  80°
Phase Difference =  80° = 80°
(ii) Angle Difference < 0°; So,
v(t) lags i(t) by 80o, or i(t) leads v(t) by 80o
EXAMPLE 13.12 (b) What is (i) the phase difference, and (ii) the phase relationship between the sinusoidal waveforms of the following sets? (b) i(t) = 15cos(t + 150°) A; v(t) = 10sin(t  20°) V
It is seen from Fig. 13.31 that v(t) starts before i(t) thus:
v(t) lags i(t) by 40o, or i(t) leads v(t) by 40o
It is seen from Fig. 13.32 that v(t) starts before i(t) thus:
v(t) lags i(t) by 80o, or i(t) leads v(t) by 80o
Solution: i(t) =  15cos(t + 150°) A = 15sin(t + 150°  90°) A = 15sin(t + 60°) A

## Slide 26
26
(i) Angle Difference = (10°)  ( 100°) = 160°
Phase Difference =  160° = 160°
(ii) Angle Difference > 0°; So,
v(t) leads i(t) by 160o, or i(t) lags v(t) by 160o
EXAMPLE 13.12 (e) What is (i) the phase difference, and (ii) the phase relationship between the sinusoidal waveforms of the following sets? (e) v(t) = 2sin(t + 10°) V; i(t) =  sin(t + 30°) A
It is seen from Fig. 13.33 that v(t) starts before i(t) thus:
v(t) lags i(t) by 110o, or i(t) leads v(t) by 110o
Solution:
i(t) =  sin(t + 30°) A = sin(t + 30°  180°) A = sin(t  150°) A
Another Answer: i(t) =  sin(t + 30°) A = sin(t + 30° + 180°) A = sin(t + 210°) A
(i) Angle Difference = (10°)  (+210°) =  200°
Phase Difference =  200° = 200°
(ii) Angle Difference < 0°; So,
v(t) lags i(t) by 200o, or i(t) leads v(t) by 200o
Practice Problem 29 ~ 33 [P583]