## Slide 1
Topics will Be Covered:
Average or Mean Value of Waveforms
RMS or Effective Value of Waveforms
Average Value and RMS Value for Rectangular Waveform
Phasor Algebra/Complex Number
APPLICATION OF COMPLEX NUMBERS IN AC CIRCUIT
Impedance: Resistance and Reactance
Admittance: Conductance and Susceptance

## Slide 2
2
Average Value or Mean Value
In case of symmetrical waveform, the average value over a full cycle is zero. Thus, the average value is calculated over half-cycle for symmetrical waveform. But for asymmetrical waveform, the average value is calculated over a full cycle.
Average value can be calculated by the following methods:
Graphical Method
Analytical or
Integral Method
Average Value: The average value of an alternating current is expressed by that dc current which transfers across any circuit the same charge as is transferred by that alternating current during the same time.
Graphical Method:
Analytical or Integral Method:

## Slide 3
3
Sine Waveform
Symmetrical Triangular Waveform
Symmetrical Sawtooth Waveform
Square Waveform

## Slide 4
4
i(t) [A]
20
EXAMPLE 13.14.1 Determine the average value for the following waveforms.
We know that the area of half-cycle of sine wave = 2  Peak Value

## Slide 5
5
Root Mean Square (RMS) or Effective Value
RMS or Effective Value: The effective or RMS value of an alternating current is given by that dc current which, when flowing through a given circuit for a given time, produces the same amount of heat as produced by the alternating current, when flowing through the same circuit for the same time.
Graphical Method:
RMS value can be calculated by the following methods:
Graphical Method
Analytical or Integral Method
Analytical or Integral Method:

## Slide 6
6
Sine Waveform
Symmetrical Triangular Waveform
Symmetrical Sawtooth Waveform
Square Waveform

## Slide 7
7
(a)
(b)
Here, Im = 20 mA
Here, Vm = 25 V
Here, Im = 4 A
EXAMPLE 13.20 Find the average value and rms values for the following sinusoidal waveforms.
(c)

## Slide 8
8
EXAMPLE 13.21 The 120 V dc source in Fig. 13.59(a) delivers 3.6 W to the load. Determine the peak value of the applied voltage (Em) and the current (Im) if the ac source [Fig. 13.59(b)] is to deliver the same power to the load.
EXAMPLE 13.20.1 Find the average value and rms values for the following sinusoidal waveforms:
(a) i(t) = 10sin(t + 30°) A
(b) v(t) = 150cos(t  60°) A
(c) i(t) =  12cos(t + 80°) A
(d) v(t) =  200sin(t  120°) mV

## Slide 9
9
Average Value and RMS Value for Rectangular Waveform
A1
A2
A3
A4
A5
A6

## Slide 10
10
EXAMPLE 13.14 Determine the average value, the rms value for the following waveforms.
(c)
(b)
(a)
(b)
(c)
(a)

## Slide 11
11
EXAMPLE 13.14.1 Determine the average value, the rms value for the following waveforms. Also, determine the average power consumption if the voltage applied across 10 ohm resistance.
Practice Problems 37 ~ 46 [Ch. 13]

## Slide 12
Chapter 14
The Basic Elements and Phasors
Phasor Algebra/Complex Number

## Slide 13
13
Vector Quantities Represent by Complex Number :
  1. Magnitude 2. Direction
Phasor Quantities Represent by Complex Number:
  1. Magnitude (RMS value for voltage and current)
  2. Direction (Phase angle)
  3. Continuously change with respect to time [such as sine and cosine waves)
Complex Number can be represented by three different ways:
  1. Polar or Phasor form
  2. Cartesian or Rectangular form
  3. Exponential form
14.7 RECTANGULAR FORM:

## Slide 14
14
14.8 POLAR OR PHASOR FORM:

## Slide 15
15
14.9 CONVERSION BETWEEN FORMS

## Slide 16
16
14.10 MATHEMATICAL OPERATIONS WITH COMPLEX NUMBERS

## Slide 17
17
Multiplication in Polar Form:
Division in Polar Form:

## Slide 18
18
Practice Problem 39 ~ 49 [Ch. 14]

## Slide 19
APPLICATION OF COMPLEX NUMBERS IN AC CIRCUIT
Instantaneous Form (Time Domain) Equation:
Phasor Form (Polar Form) Equation:
Rectangular Form (Cartesian Form) Equation:
EXAMPLE 14.27 Convert the following from the time to (i) the phasor domain, and (ii) the rectangular domain.
Time Domain
Phasor Domain
Rectangular Domain
(a) v(t) = 70.7sin(t  60o) V
(b) i(t) = 21.21cos(t + 20o) A
(c) e(t) =  200cost V
(d) i(t) = 4.5sin (t + 30o) A
= 21.21sin(t + 110o) A
= 200sin(t  90o) V
= 4.5sin (t + 210o) A
= 4.5sin (t  150o) A
15[cos()+j sin()]
3.18[cos()+j sin()]
141.42[cos()+j sin()]

## Slide 20
EXAMPLE 14.27.1 Convert the following from Cartesian form to (i) the phasor domain, and (ii) the instantaneous form for 50 Hz.
Rectangular Form
Phasor Form
Instantaneous Form
(a)
(b)
(d)
(e)
=
=
=
v(t) = ()50sin(314t  60o) V
= 70.7sin(314t  60o) V
e(t) = ()150sin(314t + 90o) V
= 212.13sin(314t + 90o) V
= 212.13cos314t V
 =250 = 314 rad/s
i(t) = ()5sin(314t 90o) A
= 7.07sin(314t 90o) A
= 7.07cos314t A
v(t) = ()100sin(314t  180o) V
= 141.42sin(314t  180o) V
= 141.42sin314t V
RMS value: 50 V
Phase Angle:
Peak Value: 70.7 V
RMS value: 150 V
Phase Angle:
Peak Value: 212.13 V
RMS value: 5 A
Phase Angle:
Peak Value: 7.07 A
RMS value: 100 V Phase Angle:  180o Peak Value: 141.42 V

## Slide 21
21
Impedance: Impedance is the ratio of voltage to current.
Impedance opposes the flow of current.
Impedance represent by Z. Its unit is ohm ().
Magnitude of Impedance:
Angle of Impedance:
Resistance (Real Part of Impedance):
Reactance (Imaginary Part of Impedance):
Reactance is the property of inductor and capacitor to oppose the flow of current. The are two reactance in electrical circuit: (i) inductive reactance (XL), and (ii) capacitive reactance (XC).
Impedance
Impedance (Z) is not a phasor quantity because for a circuit it is constant. That means impedance does not change with respect to time.
Practically,  90oz 90o

## Slide 22
22
Admittance
Admittance: Admittance is the ratio of current to voltage. Admittance is reciprocal of impedance.
Admittance is a measure of how well an ac circuit will admit, or allow, current to flow in the circuit.
Admittance represent by Y. Its unit is Siemens (S).
S
Magnitude of Admittance:
Angle of Admittance:
Conductance (Real Part of admittance):
Susceptance (Imaginary Part of admittance):
Susceptance is the property of inductor and capacitor to help the flow of current. The are two susceptance in electrical circuit: (i) inductive susceptance (BL), and (ii) capacitive susceptance (BC).
Admittance (Y) is also not a phasor quantity.

## Slide 23
23
EXAMPLE The supply voltage and current of a circuit are v(t) = 100sin314t V and i(t) = 15cos(314t120o) A.
(a) Find (i) the magnitude of impedance, (ii) the angle of impedance, (iii) the value of resistance, and (iv) the value of reactance.
(b) Find (i) the magnitude of admittance, (ii) the angle of admittance, (iii) the value of conductance, and (iv) the value of susceptance.
(c) Write the impedance and admittance in both polar and cartesian or rectangular form.
Solution: Converting current from cosine to sine, we have: i(t) = 15sin(314t30o) A.
Now, Vm = 100 V, Im = 15 A, v = 0o and i = 30o

## Slide 24
24
EXAMPLE The supply voltage and current of a circuit are V = 200V90o and I = 10A30o.
(a) Find the impedance and admittance in both polar and cartesian or rectangular form.
(b) Find (i) the magnitude of impedance, (ii) the angle of impedance, (iii) the value of resistance, and (iv) the value of reactance.
(c) Find (i) the magnitude of admittance, (ii) the angle of admittance, (iii) the value of conductance, and (iv) the value of susceptance.
Solution:

## Slide 25
25
EXAMPLE The supply voltage and impedance of a circuit are v(t) = 282.84cos314t V and Z = 2060o.
Find the current i(t).
Solution: Converting voltage from cosine to sine, we have: v(t) = 282.84sin(314t+90o) V.
Now, Vm = 282.84 V, v = 90o and Z = 20 , z = 60o
We know that:
Thus,
i(t) = 14.142sin(314t + 30o) A
EXAMPLE The supply current and impedance of a circuit are i(t) = 15sin377t V and Z = 17.32 + j10 .
Find the voltage v(t).
Solution: Converting impedance from Cartesian to Polar form:
Now, Im = 15 V, i = 0o and Z = 20 , z = 30o
We know that:
Thus,
v(t) = 300sin(377t + 30o) V

## Slide 26
26
Voltage Source Given in Different Ways
Current Source Given in Different Ways

## Slide 27
27
Impedance Diagram
Real-Axis (10o)
Imaginary-Axis
j (1 90o)
j2 =  1 (1 ±180o)
 j (1 270o =1 0o)
R = 30 
X = 40 
O
A
B
C
Z = 50 
Z
53.13o
R = 30 
X = 40 
Z = 50 
Z
53.13o
Moving Method
Parallelogram Method