## Slide 1
Topics will Be Covered:
AC Parallel Circuit: RL Parallel Circuit; RC Parallel Circuit; RLC Parallel Circuit
Admittance Calculation
Admittance Diagram
Impedance Calculation
Current/Voltage calculation
Current calculation in different branch
Phasor Diagram
Power Calculation
Power Triangle
Current Divider Rule (CDR)
Kirchhoff’s Current Law (KCL)

## Slide 2
Chapter 15
Parallel Circuits [AC]

## Slide 3
3
The total admittance of a parallel configuration is the sum of the individual admittances:
Parallel Configuration
The total impedance of a parallel configuration can be calculated as follows:
For two impedance in parallel :
Current

## Slide 4
4
The current flows through an admittance in a parallel circuit is equal to the value of that admittance (Yx) times the total current (I) divided by the total admittance (YT) of the parallel configuration.
Kirchhoff’s Current Law (KCL)
(1) The algebraic sum of the currents entering and leaving a junction (or region) of a network is zero.
(2) The sum of the currents entering a junction (or region) of a network must equal the sum of the currents leaving the same junction (or region).
Current Divider Rule (CDR)

## Slide 5
5
R-L Parallel Circuit

## Slide 6
6
R-L Parallel Circuit
R
XL
5 
10 
+

E
50V0o
IL
IR
I
Admittance
Admittance Diagram
0.2 S
+
0.1 S
0.224 S
26.57o
j
YL
YR
YT
Fig. Admittance diagram
Impedance

## Slide 7
R-L Parallel Circuit
R
XL
5 
10 
+

E
50V0o
IL
IR
I
Phasor Diagram
Current
10 A
+
5 A
0.224 S
26.57o
j
IL
IR
I
Fig. Phasor diagram
E
Practice Solution of Fig. 15.68 [Ch. 15], Problems 28 and 30
KCL:

## Slide 8
R-L Parallel Circuit
R
XL
5 
10 
+

E
50V0o
IL
IR
I
pf = (G/YT) = cosz = cos(26.57o) = 0.894 lagging
rf = (BL /YT) = sinz = sin(26.57o) = 0.447
Power Factor and Reactive Factor
Power [Total watts]
PE = EIcosz = 5011.18cos(26.57o) = 500.19 W
PR = IR2R= (E2/R)=(50V)2/5 = 500 W
Reactive Power [volt-ampere reactive]
QE = EIsinz = 5011.18sin(26.57o) = 250.1 Var
QL = IL2XL = (E2/XL)=(50V)2/10 = 250 Var
Apparent Power [volt-ampere]
SE = EI = 5011.18 = 559.5 VA
SZ = I2Z = (E2/Z)=(50V)2/4.47 = 559.72 VA
P = 500 W
Q = 250 Var
S = 559.72 VA
26.57o
Power Triangle
Instantaneous Equation
p(t) = 500(1  cos2t) + 250sin2t W
Practice Solution of Fig. 15.68 [Ch. 15], Problems 28 and 30

## Slide 9
9
R-C Parallel Circuit

## Slide 10
10
R-C Parallel Circuit
R
XC
10 
5 
+

E
50V0o
IL
IR
I
Admittance
Admittance Diagram
0.1 S
+
0.2 S
0.224 S
63.43o
j
YC
YR
YT
Fig. Admittance diagram
Impedance

## Slide 11
R-C Parallel Circuit
Phasor Diagram
Current
Practice Solution of Fig. 15.72 [Ch. 15], Problem 29
R
XC
10 
5 
+

E
50V0o
IL
IR
I
5 A
+
10 A
11.18 A
63.43o
j
IC
IR
I
Fig. Phasor diagram
E
KCL:

## Slide 12
R-C Parallel Circuit
pf = (G/YT) = cosz = cos(63.43o) = 0.447 leading
rf = (BL /YT) = sinz = sin(63.43o) =  0.894
Power Factor and Reactive Factor
Power [Total watts]
PE = EIcosz = 5011.18cos(63.43o) = 250.1 W
PR = IR2R= (E2/R)=(50V)2/10 = 250 W
Reactive Power [volt-ampere reactive]
QE = EIsinz = 5011.18sin(63.43o) =  500.19 Var
QC =  IC2XC = (E2/XC)= (50V)2/5 =  500 Var
Apparent Power [volt-ampere]
SE = EI
= 5011.18 VA
= 559.5 VA
SZ = I2Z = (E2/Z)
=(50V)2/4.47
= 559.72 VA
P = 500 W
Q = 500 Var
S = 559.72 VA
63.43o
Power Triangle
Instantaneous Equation
p(t) = 250(1  cos2t)  500sin2t W
Practice Solution of Fig. 15.72 [Ch. 15], Problem 29
R
XC
10 
5 
+

E
50V0o
IL
IR
I

## Slide 13
13
R-L-C Parallel Circuit
Example 1

## Slide 14
14
R-L-C Parallel Circuit 1
0.2 S
+
0.05 S
0.214 S
20.56o
j
YL
YR
YT
Fig. Admittance diagram
YC
0.125 S
YL YC
Impedance
R
XC
5 
20 
+
E
100V0o
IC
IR
I

XL
8 
IL
Admittance
Admittance Diagram

## Slide 15
Practice Solution of Fig. 15.77 [Ch. 15], Problem 31 to 32
R
XC
5 
20 
+
E
100V0o
IL
IR
I

XL
8 
IL
Current
Phasor Diagram
20 A
+
5 A
21.37 A
20.56o
j
IL
IR
I
Fig. Phasor diagram
IC
12.5 A
IL IC
E
100 V
KCL:

## Slide 16
16
R
XC
5 
20 
+
E
100V0o
IL
IR
I

XL
8 
IL
pf = (G/YT) = cosz = cos(20.56o) = 0.936 lagging
rf = (B /YT) = sinz = sin(20.56o) = 0.351
Power Factor and Reactive Factor
Power [Total watts]
PE = EIcosz = 10021.37cos(20.56o) = 2000.23 W
PR = IR2R= (E2/R)=(100V)2/5 = 2000 W
Reactive Power [volt-ampere reactive]
QE = EIsinz = 10021.37sin(20.56o) = 750.09 Var
QL = IL2XL = (E2/XL)=(100V)2/8 = 1250 Var
QC =  IC2XC = (E2/XC)= (100V)2/20 =  500 Var
Q = QL + QC = 750 Var
Apparent Power [volt-ampere]
SE = EI = 10021.37 = 2137 VA
SZ = I2Z = (E2/Z)=(100V)2/4.68 = 2137.75 VA
P = 2000 W
S = 2137 VA
20.56o
Fig. Admittance diagram
QC= 500 VA
QL QC
QL= 1250 VA
Power Triangle
Practice Solution of Fig. 15.77 [Ch. 15], Problem 31 to 32

## Slide 17
R-L-C Parallel Circuit
Example 2

## Slide 18
18
R-L-C Parallel Circuit 2
Impedance
R
XC
5 
20 
+
E
I = 10A20.56o
IL
IR

XL
8 
IL
Admittance
Admittance Diagram
0.2 S
+
0.05 S
0.214 S
20.56o
j
YL
YR
YT
Fig. Admittance diagram
YC
0.125 S
YC YL

## Slide 19
R
XC
5 
20 
+
E
IL
IR
I = 10A20.56o

XL
8 
IL
Current
Phasor Diagram
KCL:
0.2 S
+
2.34 A
I = 10 A
20.56o
j
IL
IR
I
Fig. Phasor diagram
IC
5.84 A
IC IL
E

## Slide 20
20
R
XC
5 
20 
+
E
46.73V0o
IL
IR
I

XL
8 
IL
pf = (G/YT) = cosz = cos(20.56o) = 0.351 leading
rf = (B /YT) = sinz = sin( 20.56o) =  0.936
Power Factor and Reactive Factor
Power [Total watts]
PE = EIcosz = 46.7310cos( 20.56o) = 437.39 W
PR = IR2R= (E2/R)=(46.73 V)2/5 = 437.11 W
Reactive Power [volt-ampere reactive]
QE = EIsinz = 46.7321.37sin( 20.56o) =  164.02 Var
QL = IL2XL = (E2/XL) = (46.73V)2/20 = 109.51 Var
QC =  IC2XC = (E2/XC) = (46.73V)2/8 =  272.84 Var
Q = QL + QC =  163.33 Var
Apparent Power [volt-ampere]
SE = EI = 46.7310 = 467.3 VA
SZ = I2Z = (E2/Z)=(46.73V)2/4.68 = 468 VA
Power Triangle
Practice Solution of Fig. 15.77 [Ch. 15], Problem 31 to 32
Fig. Phasor diagram
P = 437.39 W
S = 467.3 VA
20.56o
QC = 272.84 Var
QC QL
QL = 109.51 Var

## Slide 21
21
R6
R5
R4
R1
XL1
XC3
XL3
XL2
XC2
XC1
10 
20 
25 
15 
20 
16 
12 
8.66 
10 
5 
E = 120V0o
Is
I6
I5
I4
I3
I2
I1
Problem: For the following network:
(a) Find the conductance, susceptance and admittance for each branch.
(b) Determine the total admittance, impedance and the source current Is.
(c) Using the current divider rule, determine the currents I1, I2, I3, I4, I5, and I6.
(d) Determine the power consumption each resistor.
(e) Determine the reactive power consumption each inductor.
(f) Determine the reactive power supply by each capacitor.
(g) Find the total number of watts, volt-amperes reactive, and volt-amperes, and the power factor.

## Slide 22
22
Solution: Let,
For | Conductance [S] | Susceptance [S]
Z1 or Y1 | 0.1 | 0
Z2 or Y2 | 0 | 0.05
Z3 or Y3 | 0 | 0.04
Z4 or Y4 | 0.04 | 0.03
Z5 or Y5 | 0.024 | 0.032
Z6 or Y6 | 0.087 | 0.05

## Slide 23
23
(c) Using the current divider rule, determine the currents I1, I2, I3, I4, I5, and I6.

## Slide 24
24
(d) Determine the power consumption each resistor.
(e) Determine the reactive power consumption each inductor.
(e) Determine the reactive power consumption each capacitor.

## Slide 25
25
(g) Find the total number of watts, volt-amperes reactive, and volt-amperes, and the power factor.
Total number of watts:
Total number of volt-amperes reactive:
Total number of volt-amperes:
Power factor:

## Slide 26
26
Problem: For the following network: Find the total number of watts, volt-amperes reactive, and volt-amperes, and the power factor.
Solution:
Load 3: Power factor lagging, so circuit is reactive power is positive.
Load 4: Power factor leading, so circuit is reactive power is negative.
PT = 1600 W + 300 W + 800 W + 600 W + 1200 W = 4500 W
QT = 1200 VAR + 1066.67 VAR  450 VAR + 1600 VAR = 1016.67 VAR

## Slide 27
27
Problem: For the following network: Determine the currents Is, I1, I2, I3, I4, I5, and I6.
Solution: Here,
E = 100 V and e = 90o.
Load 1: Reactive power is negative, so circuit is capacitive and impedance angle is negative.
Load 2: Reactive power is zero, so circuit is resistive and voltage and current are in phase.

## Slide 28
28
Load 3: Power factor lagging, so circuit is inductive and impedance angle is positive.
Load 4: Power factor leading, so circuit is capacitive and impedance angle is negative.
Load 5: Reactive power is positive, so circuit is inductive and impedance angle is positive.