## Slide 1
Network Theorems
Chapter 9 [DC]
Chapter 18 [AC]

## Slide 2
2
9.4 NORTON’S THEOREM

## Slide 3
3
Any two-terminal, linear bilateral network can be replaced by an equivalent circuit consisting of a current source and a parallel resistance/impedance, as shown in the following figure.
Statement of Norton’s Theorem
RN: Norton’s equivalent resistance
IN: Norton’s equivalent current
ZN: Norton’s equivalent impedance
IN: Norton’s equivalent current

## Slide 4
4
Conversion Between Thevenin and Norton’s Equivalent Circuit
ZTh = ZN
ETh = ZNIN
ZN=ZTh
IN
ETh
ZTh

## Slide 5
5
Steps to Apply Norton’s Theorem
Step 1: | Remove that portion of the network where the Thévenin equivalent circuit is found.
Step 2: | Mark the terminals of the remaining two-terminal network.
Step 3: | Calculate RN/ZN by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance/impedance between the two marked terminals. (If the internal resistance/impedance of the voltage and/or current sources is included in the original network, it must remain when the sources are set to zero.)
Step 4: | Calculate IN by first returning all sources to their original position and then finding the short-circuit current between the marked terminals. It is the same current that would be measured by an ammeter placed between the marked terminals.
Step 5: | Draw the Norton’s equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.
Step 6: | Do the remaining required calculation

## Slide 6
6
Example 9.11 [P364] Find the Norton equivalent circuit for the network in the shaded area in Fig. 9.61.
Step 1: Remove that portion of the network where the Norton equivalent circuit is found.
Step 2: Mark the terminals (such as a and b).
Step 3: Calculate RN by first setting all sources to zero and then finding the resultant resistance between the two marked terminals (a and b).
Step 4: Calculate IN by first returning all sources to their original position then finding the short-circuit current between the marked terminals. (a and b).
Step 5: Draw the Norton equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.

## Slide 7
7
Step 1 and Step 2:
Step 3: Calculate RN:
Step 4: Calculate IN: Since there are two sources Superposition theorem has to be applied.
Consider 7 V:

## Slide 8
8
Consider 8 A:
According to Superposition Theorem
Step 5: Draw the Norton equivalent circuit:

## Slide 9
9
Example 9.12 [P365] Using the Norton Theorem to terminal a and b of Fig. 9.67, find the value of current which is passing through 9  resistor.
Step 1: Remove that portion of the network where the Norton equivalent circuit is found.
Step 2: Mark the terminals (such as a and b).
Step 3: Calculate RN by first setting all sources to zero and then finding the resultant resistance between the two marked terminals (a and b).

## Slide 10
10
Step 4: Calculate IN by first returning all sources to their original position then finding the short-circuit current between the marked terminals. (a and b).
Step 5: Draw the Norton equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.

## Slide 11
11
Step 1 and Step 2:
RN
RN
Step 4: Calculate IN: Since there are two sources Superposition theorem has to be applied.
IN1
IN1
Consider 6 V:
Problem 23 [P392] Find the Norton equivalent circuit for the portions of the networks in Fig. 9.136(b) external to branch a-b.
Step 3: Calculate RN:

## Slide 12
12
Consider 2 V:
IN2
IN2
I4
I2
V2
Step 5: Draw the Norton equivalent circuit:
0.75 A
300 
IN
RN
2 
According to Superposition Theorem
Practice Book [Ch 9] Problem: 18 ~ 23

## Slide 13
13
NORTON’S THEOREM [AC]

## Slide 14
14

## Slide 15
15

## Slide 16
16

## Slide 17
17
Practice Book Remaining Examples
And
Problem 26- 29 [Ch. 18]

## Slide 18
18
9.5 MAXIMUM POWER TRANSFER THEOREM

## Slide 19
19
A load will receive/consume/absorb maximum power from a network when its resistance is exactly equal to the Thévenin resistance of the network applied to the load. That is:
Statement of Maximum Power Transfer Theorem
When RL = RTh, the maximum power delivered to the load can be determined by first finding the current:
Power can be calculated as follows:

## Slide 20
20
For the Norton equivalent circuit in Fig. 9.84, maximum power will be delivered to the load when
Power can be calculated as follows:

## Slide 21
21
Example 9.5.1 For the following network , find the value of RL for maximum power to RL and determine the maximum power to RL.
Step 1: Remove that portion of the network where the Thévenin equivalent circuit is found.
Step 2: Mark the terminals (such as a and b) of the remaining two-terminal network.
Step 3: Calculate RTh by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance between the two marked terminals (a and b).

## Slide 22
22
Step 4: Calculate ETh by first returning all sources to their original position and finding the open-circuit voltage between the marked terminals (a and b).
Step 5: Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.

## Slide 23
23
Step 1 and Step 2: for Thévenin equivalent circuit
Step 3: Calculate RTh
Example 9.5.2 For the following network , find the value of RL for maximum power to RL and determine the maximum power to RL.

## Slide 24
24
Step 4: Calculate ETh
Since there are two sources Superposition theorem has to be applied.
Consider E1 then E2 = 0 V (shorted).
Consider E2 then E1 = 0 V (shorted).
Step 5: Draw the Thévenin equivalent circuit

## Slide 25
25
Example 9.5.2
(a) Find the Norton equivalent circuit for the network external to the resistor R for the network in Fig. 9.127.
(b) find the value of R for maximum power to R and determine the maximum power to R.
Step 1: and Step 2 for the Norton equivalent circuit.
a
b
Step 3: Calculate RN
Step 4: Calculate IN
Step 5: Draw the Norton equivalent circuit:
Practice Book [Ch 9] Problem: 18 ~ 23

## Slide 26
26
MAXIMUM POWER TRANSFER THEOREM [AC]

## Slide 27
27
Statement: Maximum power will be delivered to a load when the load impedance is the complex conjugate of the Thévenin impedance across its terminals.
Maximum Power Transfer or Impedance Matching Theorem
Then, according to maximum power transfer theorem:

## Slide 28
28
Special Situation: If the load resistance is adjustable but the magnitude of the load reactance cannot be set equal to the magnitude of the Thévenin reactance, then the maximum power that can be delivered to the load will occur when the load reactance is made as close to the Thévenin reactance as possible, and the load resistance is set to the following value:
ETh
ZTh
Xload
RL

## Slide 29
29
Maximum power received by load:
According to maximum power transfer theorem:

## Slide 30
30

## Slide 31
31
PROBLEM: Find the load impedance ZL for the networks in following Figure for maximum power to the load, and find the maximum power to the load.
Solution: Z1 = R  = 10 ; Z2 = jXL  = j8 ;
Z3 =  jXC  =  j8 ;
Step 1 and Step 2:
+

E1
I
a
Z1
Z3
Z2
Fig. (a)
b
Step 3: ZTh calculation
a
Z1
Z3
Z2
Fig. (b)
b
ZTh

## Slide 32
32
Step 4: ETh calculation
Since there are two sources, Thevenin’s voltage can be calculated by using Superposition Theorem.
+

E1
a
Z1
Z3
Z2
Fig. (c)
b
+

ETh1
Considering E1:
Considering I:
I
a
Z1
Z3
Z2
Fig. (d)
b
+

ETh2
According Superposition Theorem:
+

ETh
a
ZTh
ZLoad
b

+

ETh
a
ZLoad
b
3.9 
3.12 

## Slide 33
33
Maximum power received by load:
According to maximum power transfer theorem:
Practice Book Remaining Examples
And
Problem 39, 40, 45 and 46 [Ch. 18]

## Slide 34
Chapter 24
Poly-phase System

## Slide 35
35
An ac generator designed to develop a single sinusoidal voltage for each rotation of the shaft (rotor) is referred to as a single-phase ac generator.
If the number of coils on the rotor is increased in a specified manner, the result is a polyphase ac generator, which develops more than one ac phase voltage per rotation of the rotor.
Poly-Phase Generator
For a balanced three phase source, the peak value of voltage eAN(t), eBN(t), and eCN(t) are equal and the phase displacement from each other is 120o.
Let, the rms value of voltages eAN(t), eBN(t), and eCN(t) is Ep then these voltage are in phasor form as folows:
In a balanced system, at any instant of time, the algebraic sum of the three phase voltages of a three-phase generator is zero. That means:

## Slide 36
36
Phase Sequence or Phase Order
There are two phase sequence or phase orders:
(a) ABCsequence [B lags A by 120o and C lags B by 120o that means C lags A by 240o]
(b) ACBsequence [C lags A by 120o and B lags C by 120o that means B lags A by 240o]

## Slide 37
37
(b) Mesh or  (delta) or  (pai) connection
Three phase system can be connected two different ways:
Connection of Three-Phase System
(a) Star or Y (Wye) or T (Tee) connection
A balanced load is one which the phase impedance are equal in magnitude and in phase (also, equal in real part and equal in imaginary part).
Balanced source voltages are equal in magnitude and are out of phase with each other by 120o.

## Slide 38
38
Phase Voltages: EAN, EBN and ECN
Phase Voltages: Van, Vbn and Vcn
Line Voltages: EAB, EBC and ECA
Line Voltages: Vab, Vbc and Vca
Phase Currents: INA, INB and INC
Phase Currents: Ian, Ibn and Icn
Line Currents: IAa, IBb and ICc
Line Currents: IAa, IBb and ICc
Line Currents = Phase Currents
IAa = INA; IBb = INB; and ICc = INC
Line Currents = Phase Currents
IAa = Ian; IBb = Ibn; and ICc = Icn
Line Voltage  Phase Voltage
Star or Y (Wye) or T (Tee) connection
Let,
VP and EP: RMS value of phase voltage
VL and EL: RMS value of line voltage
IP: RMS value of phase current
IL: RMS value of line current

## Slide 39
39
Phase Voltages: EAB, EBC and ECA
Phase Voltages: Vab, Vbc and Vca
Line Voltages: EAB, EBC and ECA
Line Voltages: Vab, Vbc and Vca
Phase Currents: IBA, IAC and ICB
Phase Currents: Iab, Ibc and Ica
Line Currents: IAa, IBb and ICc
Line Currents: IAa, IBb and ICc
Line Voltage = Phase Voltage
Line Voltage = Phase Voltage
Line Current  Phase Current
Let,
VP and EP: RMS value of phase voltage
VL and EL: RMS value of line voltage
IP: RMS value of phase current
IL: RMS value of line current
Mesh or  (delta) or  (pai) connection

## Slide 40
40
Power Calculation
Instantaneous Power Equation:
Vm and Em: Peak value of phase voltage
Im : Peak value of phase current
VP and EP: RMS value of phase voltage
VL and EL: RMS value of line voltage
IP: RMS value of phase current
IL: RMS value of line current
Source Side
Load Side

## Slide 41
41
Example: The line voltage and line current of a three-phase system are 440 V and 40 A. Calculate the phase voltage and phase current for (i) star-connection, and (ii) mesh-connection.
Solution: Given: VL =440 V, IL = 40 A
For Star connection
For Mesh connection
Example 4.1.6: The phase voltage and phase current of a three-phase system are 400 V and 20 A. Calculate the line voltage and line current for (i) star or Wye-connection, and (ii) mesh or Delta-connection.
Solution: Given: VP =400 V, IP = 20 A, n=3
Star or Wye connection
Mesh or Delta connection

## Slide 42
42
Example: A 500 volts three-phase supply is connected with a -connected load having R = 18 Ω and XC = 24 Ω in series in per phase. Calculate (i) the real power, (ii) the reactive power, (iii) the apparent, (iv) the power factor and (v) the reactive factor.
Solution: Given,

## Slide 43
43
Example: A three-phase Y-connected motor draws 5.6 kW at a power factor of 0.8 lagging when the line voltage is 220 V. Determine (i) the line current and (ii) the impedance of the motor.
Solution: Given, P = 5.6 kW = 5600 W; pf = cosz = cos = 0.8 lagging, VL = 220 V
Since
Since power factor is lagging, we have
For Y-connection:
The magnitude of impedance is:
The impedance is: