## Slide 1
Summer 2021-22 Semester
Welcome to

## Slide 2
COE 2101: Introduction to Electrical Circuits
Name:
Designation:
BSc: Department (Passing Year) University Name, City, Country
MSc: Department (Passing Year) University Name, City, Country
PhD: Department (Passing Year) University Name, City, Country
Joining Month and Year in AIUB:
Previous Experience:
Email:
Official Room:
Consulting Hours:
Introduction of Course Teacher
2

## Slide 3
Basic concepts of DC circuit. Familiarizing with different components: Resistor, capacitor, Inductor, Voltage source, etc.
Familiarizing with Series, Parallel and Series-parallel circuits Basic idea about alternating quantity: Period and cycle, frequency, angular velocity, angular frequency, Sinusoidal waveform. Vector Diagram.
Ohm’s Law; Total resistance of series & parallel circuits; KVL; KCL. Equation of instantaneous voltage, current and power of an R branch, L branch, C branch, RL, RC and RLC circuits. Impedance of R, L and C; Total impedances of their series or parallel combinations. Calculation of power and power factor Brief study of transients in capacitive networks.
AC Power. Y-Delta and Delta-Y conversions; Dependent Current Source, Dependent Voltage Source; Network Theorems for DC and AC circuits: Superposition theorem Network Theorems for DC and AC circuits. Electromagnetism, Flemings hand rules,
DC generator and DC motor, Transformer, Induction motor, Synchronous generator, Alternator, Stepper Motor, Induction Motor, Universal Motor, Servo Motor, Permanent-magnet Synchronous motor, hysteresis motor, Reluctance motor, Linear motor
Course Descriptions
3

## Slide 4
Text Books
[1] R. L. Boylestad, “Introductory Circuit Analysis,” 12th Edition, Pearson Education, Inc.
[2] B. L. Theraja, A. K. Theraja, “A Textbook of ELECTRICAL TECHNOLOGY in SI
Units Volume II, AC & DC Machines,” S. Chand & Company Ltd.
[3] V.K. Mehta, Rohit Mehta, “Principles of Electrical Machines,” 2nd Edition, S. Chand
& Company Ltd.
[4] Jack Rosenblatt, M. Harold Friedman, “Direct and Alternating Current Machinery,”
C.E. Merrill Publishing Company, 1984
4

## Slide 5
Reference Books
[1] Robert P. Ward, “Introduction to Electrical Engineering”, 3rd Edition, Prentice Hall Inc.
[2] Charles K. Alexander & Mathew N.O. Sadiku, “Fundamentals of Electric Circuits”, 3rd edition, The McGraw-Hill companies.
[3] Stephen J. Chapman, “Electric Machinery Fundamentals” - 3rd Edition, McGraw- Hill International Editions
[4] Irving L. Kosow, “Electrical Machinery and Transformers”- Second Edition, Prentice –Hall India Pvt. Limited.
[5] S. K. Bhattacharya, “Electrical Machines”, McGraw Hill Education, 2014
[6] J. David Irwin and R. mark Nelms, “Basic Engineering Circuit Analysis”, Eleventh Edition, John Wiley & Sons, Inc. , 2015.
5

## Slide 6
Course Outcomes
COs | Details | Level of Domain |  |  |  | Assessed Program Outcomes (POI)#
 |  | C | P | A | S | 
CO1 | Apply information and concepts in basic electrical properties and atomic structure of materials, flow of charge, effects of temperature on resistance of a material, etc. with the familiarity of issues to calculate different electrical parameters in circuits containing both DC and AC sources. | 3 |  |  | S | P.a.1.C3
CO2 | Apply different laws, rules, methods of analysis, and theorems for the calculation of several electrical parameters in circuits containing both DC and AC sources. | 3 |  |  | S | P.a.3.C3
CO3 | Apply information and concepts of mathematics to solve single Phase AC Circuits, represent the alternating quantities and determine the power in these circuits with a range of conflicting requirements. | 3 |  |  | S | P.a.2.C3
CO4 | Apply information and concepts of rotating electrical machines in solving problems relating with voltage, current, frequency, speed, torque, power, efficiency, and flux for both AC and DC machines. | 3 |  |  | S | P.a.3.C3
C: Cognitive; P: Psychomotor; A: Affective; S: Soft-skills (CT: Critical Thinking), SL: Strongly linked; ML: Moderately linked; WL: Weakly linked # For details please check the appendix A |  |  |  |  |  | 
6
Course Outcome (COs) are statements of student actions or what the students are able to do as the course progresses.

## Slide 7
Marks Distribution
7
  Mid and Final
  Attendance (A): 10%
  Quiz (Q): 30%
  [Count best 2 Quizzes out of 3 quizzes: 15+15]
  Assignment (S) (OBE/Non-OBE)
  [One or Two Assignment]: 20%
  Mid-Exam: 40%
  Total: 100%
  Grand Total: 40% from Mid and 60% Final

## Slide 8
Assignment
Two Marks will be reduced for each day delay of submission
8
Attendance
Call your name for attendance within 30 minutes from the time of starting class.

## Slide 9
Academic Calendar
9
2022 |  | 
May | 10 – 11 | New Teachers’ orientation
 | 13 | Students’ orientation
 | 22 | First day of regular classes
 | 26 | General Meeting
 | 26 & 29 | Adding/ Dropping
 | 26 | Submission of TSF and course description
June | 2 | Automatic conversion of UW, I, blank grades of Spring 2021-22 Semester to F
 | 2 (Thursday) | Makeup of Sunday Class
 | 4 (Saturday) | Makeup of Monday Class
 | 17 | Submission of midterm exam manuscripts
 | 19 – 23 | Laboratory midterm exams
 | 25 – Jul 2 | Midterm Exam
July | 7 | Submission of midterm grades
 | 10 / 11 | Eid-Ul-Azha
 | 17 – 21 | TPE
 | 21 (Thursday) | Makeup of Tuesday Class
 | 23 (Saturday) | Makeup of Wednesday Class
 | 14 | Midterm Grades Locked
 | 24 – 28 | Pre-registration for Fall 2021-23 semester
August | 4 | Submission of final exam manuscripts
 | 6 – 11 | Laboratory Final exams
 | 11 | Submission of original midterm exam manuscripts to VC’s office
 | 13 – 20 | Final Exam
 | 27 | Submission of Final Grades
 | Sep 3 | Final Grades Locked
 | Aug 21 - Sept 10 | Semester break; Release of grades; Registration for Fall 2022 – 23
 | Sept 26 | Automatic conversion of UW, I grades of this semester to F

## Slide 10
10
Topics will Be Covered:
Electrical System
Electrical Energy Sources; Conductors or Wires
Control Elements or Switches Electrical Load
Load Represent by Passive Elements
Basic Elements of a Circuit
Basic of Circuit Elements
Passive Elements
Independent and Dependent or Controlled Sources
Defining Direction of Current and Polarity of Voltage Drop
Passive Sign Convention of Power
Branch, Junction Point, Node and Mesh (or Loop) in a Circuit
Power of Ten

## Slide 11
An electric circuit or network is an interconnection of electrical elements.
Electrical System
The components or elements of an electrical system are: (1) Source, (2) Conductors or Wires,
(3) Control Elements or Switches, and
(4) Electrical Load or Load
11

## Slide 12
DC Source
Battery (DC)
DC Generator
Lab DC Power Supply
Solar (PV) Cell
Fuel Cell
Graphical representation of DC Source
Time (t) [s]
Voltage (V) [V]
20
Electrical Energy Sources (I)
In electrical system has mainly two types of source:
  DC (Direct Current) Source
  AC (Alternating Current) Source
12

## Slide 13
Electrical Energy Sources (II)
AC Source
AC Generator in power Plant
Lab AC Power Supply
Portable AC Generator
Standby AC Generator
Wind Generation
Biogas Power Plant
13

## Slide 14
Conductors or Wires
In any electrical circuit mainly three types of wires are used:
Grounding or Earthing: Connected to any metal parts in an appliance such as a microwave oven or coffee pot. This is a safety feature, in case the hot or neutral wires somehow come in contact with metal parts. Connecting the metal parts to earth ground eliminates the shock hazard in the event of a short circuit
Hot or Positive or Phase wire: Hot wire carries the electricity from the power supply to the load
Neutral or Negative wire: Neutral wire carries the used electricity back to the power supply
14

## Slide 15
Control Elements or Switches
Control Elements or Switches are used to turn-on or turn-off a circuit.
Fuses
Circuit Breaker
Relay
Switches
SPDT
15

## Slide 16
Electrical Load
Electrical Load: The devices which consume or absorb or receive the electrical energy is called electrical load.
Hair Dryer
Refrigerator
Washing Machine
Motor
Toaster
Fan
Computer
Laptop
Vacuum
Cleaner
Water Heater
Rice Cooker
Electric Lamp
Television
Microwave
Oven
Geyser
Iron
16

## Slide 17
Load Represent by Passive Elements
17
Loads can be represented by the combination of passive elements such as Resistor, Inductor, and Capacitor.
Passive Elements As a Load: Resistance (R), Inductance (L) and Capacitance (C)
Combination of these elements: Series, Parallel and Series-Parallel
Resistance measured in ohm ()
Capacitance measured in Farad (F)
Inductance measured in Henry (H)
AM Radio Receive
17

## Slide 18
18
Basic Elements of a Circuit

## Slide 19
Basic of Circuit Elements
There are two types of elements found in electric circuits:
    (1) Passive Elements:
    (2) Active Elements:
19
(i) Resistor (ii) Inductor (iii) Capacitor
    (i) Independent Source:
    (ii) Dependent or Controlled Source:
(a) Voltage source (b) Current source
(a) Voltage Controlled Source
(b) Current Controlled Source
    (i) A voltage-controlled voltage source (VCVS)
    (ii) A voltage-controlled current source (VCCS)
            (i) A current-controlled voltage source (CCVS)
            (ii) A current-controlled current source (CCVS)

## Slide 20
Passive Elements
There are basic three passive elements: Resistor, Inductor and Capacitor
20

## Slide 21
Independent Sources (I)
21
Independent Source: An independent source is an active element that provides a specified voltage or current that is completely independent of other circuit variables.
Voltage Sources: A voltage source is an active element of a circuit that maintains a prescribed voltage across its terminals regardless current flowing in those terminals.
DC Voltage Source
AC Voltage Source
Ideal Source
Practical Source
Ideal Source
Practical Source

## Slide 22
Independent Sources (II)
22
Current sources: A current source is an active element of a circuit that maintains a prescribed current through its terminals regardless voltage across those terminals.
DC Current Source
AC Current Source
Ideal Source
Practical Source
Ideal Source
Practical Source

## Slide 23
Dependent or Controlled Sources
Dependent or Controlled Source: A dependent (or controlled) source is an active element in which the source quantity (voltage or current) is controlled by another voltage or current.
23

## Slide 24
Defining Direction of Current
24
Current Direction for a Source:
Current leaves from the positive (+) terminal of a source.
Current enters to the negative () terminal of a source.
Voltage Drop Polarities for a Load:
Current entering terminal is considered as positive (+) terminal of voltage drop in a load.
Current leaving terminal is considered as negative () terminal of voltage drop in a load.
Defining Polarities of Voltage Drop
(Vab = +); (Iab = +)
(Vab = ); (Iab = )
Symbol of Ground

## Slide 25
Passive Sign Convention of Power
If current enters through the positive polarity (or current leaves from negative terminal) of the voltage power is considered positive (i.e. P>0).
P>0 implies that the element is consuming or absorbing power.
If current leaves from the positive polarity (or current enters through negative terminal) of the voltage power is considered negative (i.e. P<0).
P<0 implies that the element is releasing or supplying or delivering power.
25

## Slide 26
Branch: A part of network which connects the various points of the network with one another is called a branch.
A branch of a circuit is any portion of the circuit that has one or more elements in series.
In the figure ab, bc, cd, de, ef, fa, bg, fg, dg, gh, hc are the various branches.
Branch, Junction Point, Node and Mesh (or Loop)
Node: A point at which two or more elements are joined is called a node. The junction points are also called node. Points a, b, c, d, e, f, g and f are node.
Mesh or Loop: A mesh or loop is a set of branches forming a closed path in a network in such a way that if one branch is removed then remaining branches do not form a closed path.
In figure loops are: a-b-c-d-e-f-a; a-b-g-f-a;
b-c-h-g-b; g-h-c-d-g; d-e-f-g-d
Junction Point: A point where three or more branches meet is called a junction point. Points b, c, d, f, and g are junction points.

## Slide 27
Test Your Knowledge
g
f
e
d
c
b
a
(a) How many branches are here? Name Them.
(b) How many nodes are here? Name Them.
(c) How many junction points are here? Name Them.
(d) How many mesh or loops are here? Name Them.
Answer: Six branches are here. They are: ab, bd, da, ag, bg, dg.
Answer: Seven nodes are here. They are: a, b, c, d, e, f, g.
Answer: Four junction points here.
They are: a, b, c, d, and g.
Answer: Four mesh or loops here.
They are: (i) a-b-c-d-a; (ii) a-e-g-d-a;
(iii) b-f-g-e-a-b; (iv) b-f-g-d-c-b;

## Slide 28
28
1.6 Power of Ten

## Slide 29
The International System of Units [SI] prefixes
Observation:
When convert smaller to larger decimal point shift to left.
When convert larger to smaller decimal point shift to right.
TABLE 1.2
Chapter 1
29

## Slide 30
When convert smaller to larger decimal point shift to left.
When convert larger to smaller decimal point shift to right.
1.8 CONVERSION BETWEEN LEVELS OF POWERS OF TEN
30

## Slide 31
EXAMPLE 1.1.1 [Similar of Problem 25]: Perform the following conversions:
a. 2000 s to milliseconds b. 0.04 ms to microseconds c. 0.06 F to nanofarads
Solution:
a. In the power of ten format: 2000 s = 2000  10-6 s
2000  10-6 s =  10-3 s
Since the power of ten will be increased by a factor of three, the multiplying factor must be decreased by moving the decimal point three places to the left, as follows:
2000  10-6 s = 2.0 ms
b. In the power of ten format: 0.04 ms = 0.04  10-3 s
0.04  10-3 s =  10-6 s
0.04  10-3 s = 40 s
Since the power of ten will be reduced by a factor of three, the multiplying factor must be increased by moving the decimal point three places to the right, as follows:
c. In the power of ten format: 0.06 F = 0.06  10-6 F
0.06  10-6 F =  10-9 F
0.06  10-6 F = 60 nF
Since the power of ten will be reduced by a factor of three, the multiplying factor must be increased by moving the decimal point three places to the right, as follows:
31

## Slide 32
EXAMPLE 1.1.2 [Similar of Problem 25]: Perform the following conversions:
a. 8400 ps to microseconds b. 0.006 km to milimeters c. 260  103 mm to kilometers
Solution:
a. In the power of ten format: 8400 ps = 8400  10-12 s
8400  10-12 s =  10-6 s
Since the power of ten will be increased by a factor of six, the multiplying factor must be decreased by moving the decimal point six places to the left, as follows:
8400  10-12 s = 0.0084 s
b. In the power of ten format: 0.006 km = 0.006  103 m
0.006  103 m =  10-3 m
0.006  103 m = 6000 m
Since the power of ten will be reduced by a factor of six, the multiplying factor must be increased by moving the decimal point six places to the right, as follows:
c. In the power of ten format: 260  103 mm = 260  103  10-3 m = 260 m
260  100 m =  103 m
260  100 m = 0.26 km
Since the power of ten will be increased by a factor of three, the multiplying factor must be decreased by moving the decimal point three places to the left, as follows:
32
Practice Book Problem [SECTION 1.8 and SECTION 1.9] Problems: 24, 26 and 27